## Slide 1
Visual Image Interpretation: Introduction
Submitted by
DR RANJITA ROY SARKAR
ASSISTANT PROFESSOR
DEPARTMENT OF GEOGRAPHY, KGTM

## Slide 2
Objectives of Visual Interpretation
• Identify land-cover features
• Recognise patterns and relationships
• Delineate boundaries
• Understand spatial arrangement
• Support mapping and field surveys
• Generate hypotheses for further analysis
2

## Slide 3
Image Tone
Tone refers to the relative brightness or darkness of an image feature.
Differences in tone may indicate differences in reflectance, moisture, vegetation density, material or illumination.
3

## Slide 4
Colour and False Colour
Colour composites assign image bands to display channels.
False-colour composites can make vegetation, water and built-up features visually distinct and often improve interpretation.
4

## Slide 5
Texture
Texture describes the frequency and arrangement of tonal or colour variations.
Examples:
• Smooth: water or uniform surfaces
• Coarse: dense built-up or rugged vegetation patterns
5

## Slide 6
Pattern
Pattern refers to the spatial arrangement or repetition of features.
Examples include:
• Regular agricultural fields
• Linear roads
• Grid-like urban streets
• Irregular natural drainage
6

## Slide 7
Shape
Shape is the geometric form of an object.
Distinctive shapes can help identify features such as:
• Runways
• Roads
• Reservoirs
• Buildings
• Agricultural plots
7

## Slide 8
Size
Size helps distinguish features when image scale or resolution is known.
A large rectangular feature may represent an industrial complex, while smaller repeated rectangles may represent residential buildings or fields.
8

## Slide 9
Shadow
Shadows provide information about height, shape and orientation.
They can help identify tall buildings, towers, trees and terrain features but may also obscure ground information.
9

## Slide 10
Site and Situation
Site refers to the physical location and characteristics of a feature.
Situation refers to its relationship with surrounding features.
Both are useful for contextual identification.
10

## Slide 11
Association
Association means identifying a feature through its relationship with other known features.
For example, a railway station may be recognised through its tracks, platforms, access roads and surrounding settlement.
11

## Slide 12
Convergence of Evidence
Reliable interpretation combines several clues rather than relying on one characteristic.
Tone + texture + shape + pattern + site + association often provide stronger identification.
12

## Slide 13
Drainage Pattern Interpretation
Drainage patterns can indicate geology, slope and structure.
Examples:
• Dendritic
• Trellis
• Radial
• Rectangular
• Parallel
Interpretation helps in geomorphology and geological mapping.
13

## Slide 14
Relief and Terrain Interpretation
Terrain can be inferred from:
• Shadows
• Contours where available
• Drainage patterns
• Slope patterns
• Image texture
Digital elevation data can strengthen terrain interpretation.
14

## Slide 15
Vegetation Interpretation
Vegetation can be identified through:
• Colour/tone
• Texture
• Pattern
• Seasonal variation
• Relationship with soil and water
Multispectral information improves discrimination.
15

## Slide 16
Water-Body Interpretation
Water bodies often appear dark in many optical bands, particularly near-infrared.
Shape, location, shoreline, sediment patterns and surrounding land use help distinguish rivers, lakes, reservoirs and ponds.
16

## Slide 17
Agricultural Land Interpretation
Agricultural areas may show regular field patterns, crop rows, irrigation structures and seasonal changes.
Field size and geometry can also provide clues about land management.
17

## Slide 18
Urban Area Interpretation
Urban areas often show:
• Bright or varied tones
• Coarse texture
• Dense road networks
• Geometric building patterns
• Strong association with transport infrastructure
18

## Slide 19
Transportation Features
Roads and railways are generally linear.
Interpretation can use:
• Width
• Surface tone
• Connectivity
• Junction patterns
• Association with settlements and bridges
19

## Slide 20
Geological Interpretation
Geological features may be inferred from:
• Lineaments
• Drainage patterns
• Relief
• Tone and texture
• Structural trends
Remote sensing is useful for regional geological reconnaissance.
20

## Slide 21
Visual Interpretation Keys
A systematic interpretation key may record:
• Feature class
• Tone/colour
• Texture
• Pattern
• Shape
• Site
• Association
• Confidence level
21

## Slide 22
Field Verification
Ground truth or field verification checks whether image interpretations match actual conditions.
It improves classification reliability and helps resolve ambiguous features.
22

## Slide 23
Scale and Resolution
Interpretation depends on image scale and spatial resolution.
Very fine features require high spatial resolution, while regional patterns may be better understood from medium-resolution imagery.
23

## Slide 24
Digital and Visual Interpretation
Visual interpretation is knowledge-driven and context-rich.
Digital classification is computational and repeatable.
Combining visual expertise with digital methods can improve mapping accuracy.
24

## Slide 25
Conclusion
Visual satellite image interpretation uses systematic clues such as tone, colour, texture, pattern, shape, size, shadow, site and association.
Strong interpretation combines image evidence with field knowledge and geographical context.
25